## Slide 1
Tapered Optical Fiber and Whispering-Gallery Mode Resonators
High-Sensitivity Optical Sensing
Jacob Juca
MTSU Quantum-Optics
07/31/26
Grivas et al., Single-mode tunable laser emission in the single-exciton regime from colloidal nanocrystals (2013).

## Slide 2
Why High-Sensitivity Optical Sensors?
Detect extremely small changes in physical and chemical environments.
Increase the interaction between light and surrounding materials.
Convert small environmental changes into measurable optical signals.
Zhang et al., Advances in Tapered Optical Fiber Sensor Structures: From Conventional to Novel and Emerging (2021).
2

## Slide 3
Optical Sensor System Overview
Input
Optical Fiber
Whispering-Gallery Mode Resonator
Optical Analyzer
Coillet et al., Microwave Photonics Systems Based on Whispering-Gallery-Mode Resonators (2013).
3

## Slide 4
Optical Sensor System Overview Explained
Input
Optical Fiber
WGM Resonator
Analyzer
Coillet et al., Microwave Photonics Systems Based on Whispering-Gallery-Mode Resonators (2013).
4
Tunable Laser Source: Provides controlled optical input
Tapered Fiber: Couples light into the resonator
Resonator: Traps light (evanescent field) in a repeating circular path
Optical Spectrum Analyzer: Measures wavelength shifts

## Slide 5
Light Confinement in Optical Fibers
Snell’s Law:
Because:
Becomes:
Eagle Group, How Does a Fiber Laser Work? (2022).
5
LSO Link, Everything You Need to Know About Single Mode Fiber Optic Cable (2025).
Core
Cladding
Outer Layer
Total Internal Reflection!

## Slide 6
Tapered Optical Fibers and Sensing
Cladding
Evanescent Field
Core
Evanescent Field:
A decaying electromagnetic field that extends beyond the fiber core and enables light–matter interaction
Soares et al., Immunosensing Based on Optical Fiber Technology: Recent Advances, (2021)
Rotating stage
Rotating stage
Cladding
Core
Heat
Yu et al., Fabrication of an Optical Fiber Micro-Sphere with a Diameter of Several Tens of Micrometers,(2014)
6

## Slide 7
Whispering-Gallery Mode (WGM) Resonators
Zheng et al., Sensing and Lasing Applications of Whispering Gallery Mode Microresonators, 2018)
Resonance occurs when the optical path length equals an integer multiple of the wavelength.
Vahala, Optical Microcavities, (2003)
Silica Microsphere
= m mode
Quality Factor: Q
7

## Slide 8
Complete WGM Optical Sensing System
Spectrum Analyzer
Power Meter
Tunable Laser
Silica Microsphere
1
2
3
4
1) Laser excites the tapered fiber
2) Evanescent coupling transfers light into the WGM resonator.
3) Environmental changes shift the resonance.
4) The optical spectrum analyzer and power meter detect the resulting signal.
Grivas et al., Single-mode tunable laser emission in the single-exciton regime from colloidal nanocrystals (2013).
8

## Slide 9
Thank you for your attention!
I am open to any and all feedback!
Jacob Juca
jj8e@mtmail.mtsu.edu
9